Adjustable thermostat and six-foot cord included.

| Watts | Volts | Total Amps (1) | CFM | Approximate Air Temperature Rise oF (oC) | Weight lb (kg) | Catalog Number |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 4000/3000 | 240/208 | 18.0/15.8 | 300 | 43/32 (24/18) | 11 (5) | 927U04000JA |  |
| 4800/3600 | 240/208 | 21.0/15.8 | 300 | 51/38 (28/21) | 11 (5) | 927U04800JA |  |
| 4000/3000 | 240/208 | 18.0/15.8 | 300 | 43/32 (24/18) | 11 (5) | 927U04000JA-MB(2) |  |
| 4800/36000 | 240/208 | 21.0/15.8 | 300 | 51/38 (28/21) | 11 (5) | 927U04800JA-MB(2) |  |

(1) Total Amps = Heating element amps and motor amps.

(2) Mounting bracket for wall or ceiling installation is included. Color is almond.

Only available with almond finish.

Not for use outdoors or wet areas.

6-20R	6-30R

Architect’s and Engineer’s Specifications

Heating Elements – Stainless steel tubular elements provide durability.

Housing – Heavy 22-gauge galvanized steel cabinet has a polyester powder paint finish.

Inlet/Outlet Grilles – Inlet and discharge grilles are made of industrial gauge steel and both have a finger-proof design for added safety.

Built-in Controls – Unit comes with an automatic reset thermal cutout and adjustable thermostat.

Fan Motor – Durable factory-lubricated fan motor with 300 CFM.

Heavy-duty Cord – A six-foot heavy-duty cord is provided with each heater. The handle of the heater may be used as reel for the cord set. The 4000 watt heater is provide with a 3-pronged, 20A 250 VAC NEMA type #6-20R plug; 4800 watt heater with a 3-pronged, 30A 250VAC #6-30R plug.

Mounting Bracket – Mounting bracket for wall or ceiling installation included on heater ending with (MB).